## Slide 1: two-wheeled self-balancing ultrasonic obstacle-avoidance transport vehicle based on an Arduino microcontroller
Zihan Gao
I did before: Based on stm32, with no bluetooth wireless control and unbalanced, didn’t finish

## Slide 2: Porblem&Aim
Problem:
A four-wheeled transport vehicle has a large size and requires a wide space for turning, making it unsuitable for uneven terrain.
In contrast, a two-wheeled transport vehicle is compact and highly maneuverable, capable of rotating in place and adapting to irregular ground surfaces.
Aim:
To place a cup of water on the vehicle and ensure that it can move flexibly without spilling the water, thereby demonstrating system stability.

## Slide 3: Hardware
Arduino UNO
TB6612 Motor Drive
HC-SRO4 ultrasonic
MPU6050 imu
LM2596S voltage decrease
JGA25-370 Encoder Motor
HC-05 bluetooth

## Slide 4: Coding
Plan:
Sensing Layer:
IMU for pitch angle estimation;
Ultrasonic sensor for obstacle detection.
Control Layer:
Arduino UNO
PID control algorithm
obstacle-avoidance logic
Execution Layer:
motor driver for differential wheel control
wireless controller for user interaction
So far:
Next step:
PID control algorism
Rotation algorism
obstacle avoidance
and keep adusting values...

## Slide 5: Software require
Arduino IDE
  Android Studio
PCB software
CAD software if needed

## Slide 6: schematic

## Slide 7: Pin arrangement
Digital PIN | Connection | Function
0 | NO Connection | TX/serial communication/upload
1 | NO Connection | RX/serial communication/upload
2 | Motor A PIN1 | INT[1], encoder interrupt trigger pin
3 | Motor B PIN1 | INT[0], encoder interrupt trigger pin
4 | HC-05 RX | Blue tooth RX pin
5 | HC-05TX | Blue tooth TX pin
6 | TB6612 BIN2 | Motor B direction control
7 | TB6612 BIN1 | Motor B direction control
8 | HC-SRO4 ECHO | ultrasonic echo
9 | HC-SRO4 TRIG | ultrasonic trigger
10 | TB6612 PWMB | PWM output, Motor B speed control
11 | TB6612 PWMA | PWM output, Motor A speed control
12 | TB6612 AIN1 | Motor A direction control
13 | TB6612 AIN2 | Motor A direction control
Analogue PIN |  | 
0 | Motor A PIN2 | Use as a digital pin, working with Digital PIN 2
1 | Motor B PIN2 | Use as a digital pin, working with Digital PIN 3
2 | NO Connection | 
3 | NO Connection | 
4 | NO Connection | 
5 | NO Connection | 
Other Pin |  | 
SCL | MPU6050 SCL | 
SDA | MPU6050 SDA | 
AREF | NO Connection | 
IOREF | NO Connection | 
RESET | NO Connection | 
3.3V | NO Connection | 
5V | VCC/TB6612 STBY | 
Vin | LM2596S OUT+ | 
GND | GND | 

## Slide 8: Gantt Chart

## Slide 9: Future works
1. PID Control Optimization and Adaptive Tuning
2. Obstacle Avoidance& path planning(if have time)
3. Data Visualization(if have time)
4.Hardware Upgrade(Arduino uno may not enough)
5. Engineering and Application Expansion: The platform can be extended into a small-scale delivery or transport robot